## Slide 1: Embedded computing
Master ATIAM - Informatique
Philippe Esling (esling@ircam.fr)
Maître de conférences – UPMC
Equipe représentations musicales (IRCAM, Paris)
UDOO – Single-board and microcontroller

## Slide 2: Single-Board Computer vs. Microcontroller
Arduino UNO
Microcontroller (MCU)
Raspberry Pi
Single-Board Computer

## Slide 3: What can you do with this ?
Jasper – Voice Controller powered by Rpi https://jasperproject.github.io
LED Cube - http://www.instructables.com/id/Led-Cube-8x8x8/
Flamethrower Jack-O-Lantern - http://www.instructables.com/id/Flamethrowing-Jack-O-Lantern/
Arduino RC- Lawnmower http://www.instructables.com/id/Arduino-RC-Lawnmower/
Fermentation Monitoring - https://www.sparkfun.com/tutorials/131
Raspberry Eye - https://hackaday.io/project/865-raspberry-eye

## Slide 4: Why so popular?
They are cheap
They sense and manipulate the physical world
  GPIO pins (reading values/sending instructions)
GPIO = General Purpose Input/Output

## Slide 5: Internet of Things (IoT)
Connection of embedded computing devices
  Home Automation
  Augmented Reality
Connecting non-computer devices
  Home Entertainment
  Aquariums
  … your fridge ?!
  Etc.

## Slide 6: Single-Board Computer vs. Microcontroller What is the difference?
Microcontrollers
Single-board Computers

## Slide 7: Single-Board Computer vs. Microcontroller Defining Features
Single-board computer
  Lots of processing power
  Operating system (Linux, Android)
  Monitor Connection
  Cheap, “weak” computer
Microcontroller
  Devoted to having GPIO pins
  Low power, quick boot
  Very cheap
Raspberry Pi
Arduino

## Slide 8: Micro-controller ?
A single chip has to emulate a small computer
  Processor, memory, and input/output

## Slide 9: Microcontrollers Arduino
 | Arduino Uno | Arduino Mega2560 | Arduino Nano (ATmega328)
Microcontroller | ATmega328 | ATmega2560 | ATmega328
Flash Memory | 32KB | 256KB | 32KB
Clock Speed | 16MHz | 16MHz | 16 MHz
RAM | 2KB | 8KB | 1KB
Price (approx, USD) | $24.95here | $45.95 here | $34.99 here
Digital I/O Pins | 14 | 54 | 14
http://arduino.cc/

## Slide 10: Arduino Microcontroller

## Slide 11: Arduino Microcontroller
GPIO Pins !

## Slide 12: How do we use this ?
Working with these devices requires
  Programming
  Electronics

## Slide 13: First Challenge Programming – Simplifying Aspects
Pre-written Libraries
Code Examples
  https://github.com/
Community help (Forums, StackExchange)
Free online courses
  Search for “MIT Arduino Course”
  Programming courses on:
    Khan Academy
    Coursera
    Udacity

## Slide 14: Second Challenge Electronics – the hard part
Difficult to get started
Easy to make mistakes
  Some mistakes cannot be undone
Often needs additional equipment:
  Soldering Iron
  Voltmeter
  Oscilloscope

## Slide 15: Electronics Simplifying Aspects
Starter Packs and Kits
  Contain a minimum number of electronic components that you may need
Microcontroller Attachments
  Shields (for Arduino)
    Motor shields, sensor shields
  Capes (for Beagleboard)
  BoosterPacks (TI LaunchPad)
Notes: -Simplify things for beginners and prototyping
-Somewhat pricey
-You would not use it for the final product, because it has components that you don’t need

## Slide 16: Electronics Simplifying Aspects
A lot of electronics come like this:
Solution: Breakout boards: pre-soldered breadboard-ready electronics:
Source:
http://elecshop.blog.com/files/2014/01/313-44-TQFP.jpg
http://www.renesas.com/media/press/news/2010/20101006.jpg

## Slide 17: Microcontroller Expansion Boards features
Communication Cable Attachments
Programmer
Buttons
Power Supply Connectors
Pin connectors
On-board Sensors
  (accelerometers, real-time clocks, temperature sensors)

## Slide 18: How to use Arduino ?
  Download & install the Arduino environment (IDE)
  Connect the board to your computer via the USB cable
  Launch the Arduino IDE
  Select your board
  Select your serial port
  Open the blink example
  Upload the program

## Slide 19: Arduino IDE

## Slide 20
todbot.com/blog/bionicarduino
???
Profit

## Slide 21: Microcontrollers Arduino IDE - Programming
http://arduino.cc/

## Slide 22: Arduino terminology

## Slide 23: Bare minimum code
void setup() { // put your setup code here, to run once:
}
void loop() { // put your main code here, to run infinitely:
}

## Slide 24: Bare minimum code
setup :
  Called only when Arduino is powered on or reset
  Used to initialize variables and pin modes
loop :
  Runs continuously till the device is powered off.
  Main logic of the code goes here.
  A form of while(True) for micro-controller

## Slide 25: Digital I/0
pinMode(pin, mode)
  Sets pin to either INPUT or OUTPUT
digitalRead(pin)
  Reads HIGH or LOW from a pin
digitalWrite(pin, value)
  Writes HIGH or LOW to a pin

## Slide 26: PinMode
A pin can be set as input or output
(All I/O pins can serve both mode)
pinMode function.
pinMode(13, OUTPUT);
// sets pin 13 as output pin
pinMode(13, INPUT);
// sets pin 13 as input pin

## Slide 27: Reading/writing digital values
digitalWrite(13, LOW);
// Makes the output voltage on pin 13 , 0V
digitalWrite(13, HIGH);
// Makes the output voltage on pin 13 , 5V
int buttonState = digitalRead(2);
// reads the value of pin 2 in buttonState

## Slide 28: Analog to Digital (ADC) Conversion
Analog ?
Continuous range of voltage values
Based on electrical in/outs
Why convert to digital ?
Because our microcontroller only understands digital.

## Slide 29: ADC in Arduino
The Arduino Uno board contains pins for ADC
10-bit analog to digital converter
Map input voltages between 0 and 5 volts into integer values between 0 and 1023

## Slide 30: Analog Value to Digital ?

## Slide 31: Digital? Analog?
Digital has two values: on and off
Analog has many (infinite) values
Computers don’t really do analog, they quantize
Remember the analog input pins---here’s how they work
todbot.com/blog/bionicarduino

## Slide 32: Signal quantization

## Slide 33: Reading/Writing Analog Values
analogRead(A0); // used to read the analog value from the pin A0
analogWrite(2,128);

## Slide 34: ADC Example
// These constants won't change. They're used to give names to the pins used: const int analogInPin = A0; // Analog input pin that the potentiometer is attached to const int analogOutPin = 9; // Analog output pin that the LED is attached to int sensorValue = 0; // value read from the pot int outputValue = 0; // value output to the PWM (analog out) void setup() { // initialize serial communications at 9600 bps: Serial.begin(9600); } void loop() { // read the analog in value: sensorValue = analogRead(analogInPin); // map it to the range of the analog out: outputValue = map(sensorValue, 0, 1023, 0, 255); // change the analog out value: analogWrite(analogOutPin, outputValue); // print the results to the serial monitor: Serial.print("sensor = " ); Serial.print(sensorValue); Serial.print("\t output = "); Serial.println(outputValue); // wait 2 milliseconds before the next loop for the analog-to-digital converter to settle delay(2); }

## Slide 35: Arduino Timing
delay(ms)
  Pauses for a few milliseconds
delayMicroseconds(us)
  Pauses for a few microseconds
More commands: arduino.cc/en/Reference/HomePage

## Slide 36: Microcontrollers Thousands Others
Beetle
Pinguino PIC32
Ruggeduino
Gamebuino
Some of these had limited production runs or have been discontinued.
Freescale Freedom
Teensy
Beetle: http://www.dfrobot.com/wiki/index.php/Beetle_SKU:DFR0282
Nanode: http://www.nanode.eu/
Pinguino PIC32: https://www.olimex.com/Products/Duino/PIC32/PIC32-PINGUINO/open-source-hardware
Ruggeduino: http://www.ruggedcircuits.com/ruggeduino/
Gamebuino: http://gamebuino.com/
Freescale Freedom: http://www.freescale.com/webapp/sps/site/overview.jsp?code=FREDEVPLA
Teensy: https://www.pjrc.com/teensy/

## Slide 37: Single-Board Computer vs. Microcontroller Examples of Embedded Systems
Image Source
http://pixshark.com/raspberry-pi-model-b-schematic.htm
http://images.studica.com/images/product/arduino/9a9b5c9e479e1a5b237b41a173d34dcfimage472x354_72_200x.gif
Broadcom BCM2835
CPU, GPU, RAM
Storage
ATMega328
CPU, RAM, Storage

## Slide 38: Single-Board Computers Raspberry Pi
 | Raspberry Pi Model B | Raspberry Pi 2
Processor | ARM1176JZF-S core | Quad-core ARM7
Flash Memory | None | None
Clock Speed | 700 MHz | 800 MHz
RAM | 512MB | 1 GB
Price (approx, USD) | $39.95 | $35.00
Other Features | 2x USB ports 26x GPIO pins | 4x USB2.0 40x GPIO pins
Image Source: http://www.techradar.com/news/computing-components/peripherals/raspberry-pi-2-outed-with-faster-cpu-double-ram-and-windows-10-support-1283075
http://www.raspberrypi.org/

## Slide 39: Raspberry Pi ?

## Slide 40: Raspberry Pi ?
But also …
Powerful CPU
Screen display
Audio (sometimes)
Ethernet / WiFi

## Slide 41: Raspberry Pi ?
But also …
Powerful CPU
Screen display
Audio (sometimes)
Ethernet / WiFi
External storage
Operating system (Linux)
Ease of use/debug
Computing / RAM power
And most importantly

## Slide 42: Single-Board Computers
Properties
  Processor Speed (Ghz, Multiple core)
  RAM (speed of RAM)
  Video Card (Home entertainment)
  On-board storage (FLASH)
  Hard-drive storage
  GPIO pins
  Features
    Audio jack
    IR remote
    Blue tooth
    Other connectors

## Slide 43: Single-Board Computer vs. Microcontroller
Arduino UNO
Microcontroller (MCU)
Raspberry Pi
Single-Board Computer

## Slide 44: Single-Board Computer vs. Microcontroller
Arduino UNO
Microcontroller (MCU)
Raspberry Pi
Single-Board Computer

## Slide 45: Single-Board Computer vs. Microcontroller
UDOO
Single-Board Computer
+ Arduino Microcontroller (MCU) !

## Slide 46: Single-Board Computers UDOO
 | UDOO Quad
Processor | Quad-core 1GHz
Flash Memory | None (SATA connector)
RAM | 1 GB DDR3
Other Features | 2x USB port WiFi Module 76 x GPIO pins Analog Audio and Mic
Price (approx, USD) | $135.00
http://www.udoo.org/

## Slide 47: UDOO

## Slide 48: UDOO
POWER

## Slide 49: UDOO
POWER
ANALOG
IN/OUT

## Slide 50: UDOO
POWER
ANALOG
IN/OUT
DIGITAL
IN/OUT

## Slide 51: UDOO
POWER
ANALOG
IN/OUT
DIGITAL
IN/OUT
PWM
Pulse Width
Modulation

## Slide 52: UDOO - PureData
https://github.com/irllabs/Udoo
PureData has a special distribution for UDOO
You can find pre-compiled versions for it or compile it
This PureData version can use two objects
Find more informations and tutorials at
[gpio] allows a direct interaction with pins
[comport] is a serial data transfer extern (interact with Arduino code)
https://www.udoo.org/forum/threads/guide-compile-pure-data-extended-on-udoo.478/

## Slide 53: UDOO – PD
Project - Theremin of light

## Slide 54: UDOO – PD
Project - Theremin of light
int IRpin = A0;
int distance = 0; int msg = 0;
void setup() { Serial.begin(115200); }
void loop()
{
distance = analogRead(IRpin);
if (distance < 100) { distance = 100; }
else if (distance > 900){ distance = 900; }
msg = map(distance, 100, 900, 0, 255); Serial.write(msg);
}